## Slide 1: Robot Framework Introduction
自動化開發與認證課
David_Zhu
2022/5/10

## Slide 2
Agenda
Robot Framework Introduction
Automation Tool Introduction
Demo

## Slide 3: Python – Robot Framework
Robot Framework
  Base on Python Language to implement.
  Robot Framework program grammar easy for automation used.
  Robot Framework have below function.
    Automation test report creation
    Automation test case execution
    Pass / Fail result determination

## Slide 4: Python – Robot Framework
Robot Framework Format
*** Settings ***
Library value
Resource value
Variables value
Suit Setup value
Suit Teardown value
*** Variable ***
${Var} value
*** Keyword ***
Function_Name Action
*** Test Case ***
Test_Case Step_Action

## Slide 5: Python – Robot Framework
Robot Framework (Settings block)
    Used for package import
    Keyword
      - Library : Import python package
      - Resource : Import robot package
      - Suit Setup : Execute the test preliminary work before test
      - Suit Teardown : Recovery the setting after test
Settings | Value | Value | Value
Library | ../util/ipmitool/IPMI_util.py |  | 
Resource | ../util/ipmitool/IPMI_Power_Control.robot |  | 
Variables | ../setup.py |  | 
Suit Setup | Launch Browser and Login GUI |  | 
Suit Teardown | Close Browser |  | 

## Slide 6: Python – Robot Framework
Robot Framework (Variable block)
    Used for variable declare.
    Variable can be named by user.
    Used ${ } format to define variable name.
Variable | Value | Value
${xpath_hardware_status_heading} | //*[@id="main"]/div/div/aside[1]/div/section/ul/li[11]/a | 
${BMCWeb} = | https://${BMCIP} | 

## Slide 7: Python – Robot Framework
Robot Framework (Keyword block)
    Function declare for used.
    Function can be named by user.
    Used Robot Framework Keyword [Arguments] to define function arguments.
Keyword | Action | Argument | Argument | Argument | Argument | Argument | Argument
Chassis Power On | [Arguments] | (Optional) |  |  |  |  | 
 | ${result} = | ipmicmd | lanplus | ${USERID} | ${PASSWORD} | ${BMCIP} | chassis power on
 | Log To Console | ${result} |  |  |  |  | 
 | Should Contain | ${result} | Up/On |  |  |  | 
 | …………… |  |  |  |  |  | 

## Slide 8: Python – Robot Framework
Robot Framework - In common use Keyword
  Run Keyword and Return Status
  Wait Until Page Contains Element
  Should Be Equal
  Set Test Variable
  Run Keyword If
  Click Element
  Double Click Element
  Sleep
  Element Attribute Should Contain Text

## Slide 9: Python – Robot Framework
Robot Framework (Test Case block)
    Test Case step defined.
    Test Case check point defined.
    Test Case step can call Function (Keyword) what you want to test.
    Used Robot Framework Keyword [Documentation] to define test description
Test Case | Action | Argument | Argument
BMC Web Power Off Server Immediate | [Documentation] | Verify BMC Power Control From WebUI | 
 | Wait Until Element Is Visible | //*[@id="main"]/div/header/label | 
 | Click Element | //*[@id="main"]/div/div/aside[1]/div/section/ul/li[11]/a | 
 | Sleep | ${OSDelay} | 
 | Capture Page Screenshot |  | 
 | …………… |  | 

## Slide 10: Python – Robot Framework
Robot Framework – Redfish PATCH Test
Settings : Used to Import the python package or other Robot script witch need to used.
Test Cases : Used to design the test step of the test target, it can be assigned the multiple test case to do the sequential test.
Redfish Function test : Call Redfish function to do the PATCH test, used Robot Framework Keyword “Should Be Equal ” to compare the response.

## Slide 11: Python – Robot Framework
Robot Framework- Web UI Test
Variables : Used for variable declare, If test on WebUI, it can used to declare the WebUI source code. (Press F12 to get the Web item Xpath)
WebUI Test : After WebUI Test finished, can used Robot Framework Keyword “Capture Page Screenshot” to capture the Web page and then Close the Broswer
WebUI Control : Base on Selenium2 Framework and used Robot Framework Keyword “Click Element ” control WebUI to click items.

## Slide 12: Python – Robot Framework
Selenium Framework- Web UI Control
Web Source code : Press F12 to get the Web item Xpath, Selenium framework need to get the web item Xpath and depend on WebDriver to control the web.
Chrome : ChromeDriver
Firefox : FirefoxDriver

## Slide 13
Automation Tool Introduction

## Slide 14: Automation Tool Introduction
Automation Related Technical
- Environment requirement as below
  Windows OS
  Python 3
  Robot Framework
    For automation test and test report creation
  Ipmitool
    For IPMI command used
  Redfishtool
    For REST method GET / POST / PATCH / DEL used
  Selenium2Library
    For Web GUI automation test control (Web motion control)

## Slide 15: Automation Tool Introduction
Automation Tool Environment Setting
  The newest python installation.
  Need to execute "pip install -r requirements.txt" at the BMC_Automation_Test folder to install the related python package.
  "BMC_Automation_Test/drivers" folder need to add the environment variable on Windows OS.
  "util/ipmitool" folder need to add the environment variable on Windows OS.
  Google Chrome need to used Version 100.0.4896.127 above.

## Slide 16: Automation Tool Introduction
Automation Tool Setup and Run
  Set the related parameter about BMC IP, Username, Password and others on GUI interface.
  Execute the GUIsetup.py by command "Python GUIsetup.py" to launch the GUI interface.
  Execute the command "robot TestCase\\${TestCaseName}" to used by command line.
  After test finished, you can check the Test report under the "BMC_Automation_Test" folder.
  This tool can test BMC function which TestCase you add in the TestCase folder.

## Slide 17: Automation Tool Introduction
Automation Tool Architecture
Criteria Define
Test Case Define
Web Driver
Related Tool
GUI Setup
Test Report

## Slide 18: Automation Tool Introduction
Automation Tool GUI
Test Case Selection
Configure Setup
BMC Connection Check
Start Test

## Slide 19: Automation Tool Introduction
Automation Tool Test Run

## Slide 20: Automation Tool Introduction
Automation Tool Test Report

## Slide 21: Automation Tool Introduction
Demo